## Slide 1
16 January 2026
Telkom | 2nd draft National Table of Frequency Allocations: Oral hearings
Notes: 1

## Slide 2
Introduction
Telkom welcomes the opportunity to present to the Authority on the 2nd draft National Table of Frequency Allocations, 2025 (NTFA-25).
The NTFA is the most fundamental spectrum instrument that guides all current and future spectrum use in South Africa. NTFA-25 is long overdue; Telkom recommends that updating should occur no later than 12 months after a WRC.
Telkom is grateful that most of its comments to the 1st draft NTFA-25 have been incorporated into the 2nd draft version. Telkom’s submission to the 2nd draft NTFA-25 aims to assist the Authority in addressing some key remaining issues.
The 2nd draft NTFA-25 was published on 7 Nov 2025 with due date for comments 11 December 2025. Due to limited time, Telkom could not completely review the 2nd draft and respectfully requests the Authority to ensure that the final version is accurate and consistent to ensure regulatory certainty.

## Slide 3
Internal Use
Specific Comments
5
1
Sub 1 GHz bands (450-470 MHz and 694-790 MHz)
Telkom supports the consideration of PPDR within the range 380-470 MHz, which includes the IMT450 band. This should however follow a public process and may require an amendment of the IMT450 Radio Frequency Spectrum Assignment Plan (RFSAP).
References to IoT and M2M under IMT are only examples; IMT also includes, for example, broadband services. IMT use must remain technology/service neutral.
Telkom agrees with the addition of HIBS to the relevant frequency bands in the range 694-960 MHz. Telkom however requests that the introduction of HIBS be done through a coordinated public process, which includes the amendment of the relevant RFSAPs. HIBS should be considered as part of the existing IMT spectrum licences and should not be licensed separately.
Whereas Telkom supports the consideration of PPDR in the range 694-790 MHz, the upcoming licensing of IMT750 in SA will impact the availability of the SADC recommended PPDR spectrum. Certainty in the future availability of the IMT750 spectrum is critical in the upcoming licencing process. A public process for PPDR considerations is therefore essential.
Notes: 20

## Slide 4
Internal Use
Specific Comments
5
1
Frequency band 1427-1518 MHz (IMT1500)
In line with the IMT1500 RFSAP, it is indicated in the 2nd draft NRFP-25 that the IMT1500 band can be used for either SDL or TDD. This however is not practical as sharing between SDL and TDD, without sufficient guardbands between assignments, will not be possible.
This band is included as part of the upcoming 2nd IMT licensing process; the issue of SDL vs TDD must therefore be resolved before the band is made available for licensing. This will require an amendment of the IMT1500 RFSAP.
Telkom recommends that the IMT1500 band be used for SDL only, in line with its use in Europe.
Notes: 20

## Slide 5
Internal Use
Specific Comments
5
1
Frequency band 1880-1900 MHz (DECT band)
The reference to ECC Report 196, which deals with number portability, is irrelevant and must be clarified/corrected.
A reference is made to an ICASA RFSAP, which recognises DECT systems - as there is no known RFSAP relating to DECT systems, this must be clarified.
A reference to “ITU-R Resolution 59 (Rev. WRC-19)” was added next to the DECT application. This Res deals with studies on frequency bands for ENG systems. It is not clear if the band is considered for ENG or if the “DECT-based audio applications” are relevant in this regard. This needs further clarification.
A reference to ITU-R Report BT.2338 has been added in the band 694-790 MHz, which deals with services ancillary to broadcasting and program making. Its relevance to the band 1880-1900 MHz needs verification.
Notes: 20

## Slide 6
Specific Comments
5
1
Frequency band 1900-1920 MHz (FRMCS)
The application of FRMCS in the band 1895-1951 MHz should be 1895-1915 MHz.
The reference to “PMR for GSM-R (paired with 874.4-880.0 MHz)” is not relevant in this band and should be deleted. Also, the reference to “PMR for GSM-R (1900-1910 MHz)” should be “RMR/FRMCS”, in line with terminology used in CEPT Report 90.
The stipulated FRMCS band also differs from the band being considered i.e. 1895-1915 MHz.
Compatibility with IMT in the 2100 MHz band is key and must be ensured.
References to ECC/DEC/(20)03 and ECC/REC/(23)01, which relates to FRMCS, could be added to the NRFP-25.
If the band 1895-1915 MHz is earmarked for RFMCS, the reference to IMT1900 (1900-1920 MHz) could be deleted.
Internal Use
Notes: 20

## Slide 7
Specific Comments
5
1
Frequency band 3600-4200 MHz
The Authority added IMT to the band 3600-3800 MHz, in line with the outcome of WRC-23, which is supported.
Telkom supports the development of a RFSAP for this band. Any mobile/IMT deployment in this band must however not happen until the RFSAP has been prescribed.
With the division of the band 3600-4200 MHz into two sub-bands, the reference to the licensing/registration of C-band earth stations in the sub-band 3600-3800 MHz should be deleted.
The need to highlight the licensing of C-Band earth stations in the band 3800-4200 MHz is not clear as all use of spectrum, both transmit and receive, needs a spectrum licence, which includes satellite earth stations, unless it has been exempted by the Authority. This need further clarification.
Internal Use
Notes: 20

## Slide 8
Internal Use
Specific Comments
5
1
Frequency band 6425-7125 MHz (Upper 6 GHz)
CEPT studied sharing between IMT and WAS/RLAN and indicated, amongst others, that sharing between high power outdoor IMT and WAS/RLAN LPI is not feasible (CEPT Report 366). The RSPG proposed band segmentation - bottom 160 MHz for WAS/RLAN priority access and the top 540 MHz for IMT priority access. The 160 MHz serves as a guard band and should be reviewed after WRC-27, specifically linked to the outcome of agenda item 1.7. Use of WAS/RLAN in the band 6425-6585 MHz depends on IMT identification in 7 GHz.
Telkom supports the identification of the entire Upper 6 GHz band for IMT, as per SA and ATU positions at WRC-23 (while WAS/RLAN uses Lower 6 GHz). IMT in 6 GHz requires up to 200 MHz channels (for 6G). The outcome of WRC-27 cannot be predicted and noting the concerns in the identification of additional IMT spectrum in the 7 GHz band (in SA) noting the need for PTP links.
Allowing WAS/RLAN access to the Upper 6 GHz band, or part of this band, through the NRFP-25 will be irreversible when the spectrum is required for IMT.
The use of the Upper 6 GHz band for AFC is being considered by OFCOM but is not part of the current SA DSA process pertaining to the 4 GHz and Lower 6 GHz bands.
Notes: 20

## Slide 9
Internal Use
Specific Comments
5
1
Frequency band 21.2-23.6 GHz (23 GHz)
Telkom recommends that the BSS allocation in the band be deleted for the following reasons:
The 23 GHz band is critical for fixed links, including backhaul for mobile base stations. Sharing between ubiquitously deployed BSS small antenna receivers and fixed links will be difficult.
The Ku-band (11 GHz) is used for DTH broadcasting in South Africa making the need for 23 GHz unclear.
A dedicated satellite operating in the 23 GHz band serving South Africa will be required, which may not be economically viable noting other national and regional satellite projects.
Deleting BSS from this band will provide regulatory certainty for the use of the 23 GHz band for fixed links, also noting the potential impact of IMT to be deployed in the 26 GHz band in future.
Notes: 20

## Slide 10
Internal Use
Specific Comments
5
1
National footnotes (NF9, NF14 and NF16)
Telkom requests the Authority to review the tables in these three FNs to amend certain editorial and factual inconsistencies.
NF9 - certain WRC resolution dates have not been updated; the overlap between 1900 MHz and 2100 MHz (TDD) have not been addressed; and the 45 GHz band was not added.
NF14 - the ITU-R Rec Annex numbers for Lower and Upper 8 GHz bands have not been corrected in NF14 (only in the table of allocations); the 52 GHz band must be added; and the 57 GHz band must be changed to 62 GHz and divided into the three sub-bands as per the table of allocations.
NF16 - Telkom recommends that the 200 watt e.i.r.p. maximum power option be reviewed as it is no longer contained the RFSR. Telkom also recommends that all WAS/RLAN bands be added to NF16. Also, the use of the band 17.1-17.3 GHz for WAS/RLAN must be verified.
Telkom also recommends that frequency bands above 92 GHz be considered for fixed links and added to FN14 (and the table). Examples include:
ECC/REC(18)01 for the bands 130-134 GHz, 141-148.3 GHz, 151.5-164 GHz, and 167-174.8 GHz;
ECC/REC(18)02 for the bands 92-94 GHz, 94.1-100 GHz, 102-109.5 GHz, and 111.8-114.2 GHz;
ECC Report 282 applies to these bands for PTP links.
Notes: 20

## Slide 11
Thank you